## Slide 1: Embedded Linux
2023/04/25
劉正文

## Slide 2: Linux
Hard real-time 作業系統伴隨著巨大的維護成本
Linux作為通用作業系統開發的，其核心在即時處理能力上先天不足
部分網路開發社群將其改造能在一定程度上成為即時作業系統
Linux 核心主流的解決方案就是 PREEMPT_RT
Linux 核心從對一個即時行程 (realtime process) 予以排程，到該即時行程實際投入執行之間的延遲時間 (稱為 latency) 行為上”不可預測”，因此無法給予有著硬即時需求的任務任何保證，自然不可能滿足即時需求
PREEMPT_RT 將中斷處理轉化為核心執行緒，保證它不再佔用任意 context，這保證即便中斷被即時行程搶佔，也不會連累無辜地被它佔用核心堆疊的行程

## Slide 3: Solution
RTOS
  FreeRTOS
  RTEMS
  RT-Linux
  VxWorks
  μC/OS-Ⅱ
LEON3
  SPARC V7、V8
Raspberry pi
  Broadcom BCM2837
  1.2 GHz 64-bit quad-core ARM Cortex-A53
SAMRH71
  Rad-Hard Arm® Cortex®-M7 Microprocessor

## Slide 4: SAMRH71

## Slide 5: Raspberry Pi 3B

## Slide 6: LEON3 UT-699

## Slide 7: LEON Linux Overview

## Slide 8: GRLIB IP-cores
LEON3, LEON4, LEON5 (all in single or multicore configurations)
MMU, V8, FPU
GPTIMER System Clock Timer
IRQMP or IRQAMP interrupt controller
APBUART system console
GRETH 10/100 and 10/100/1000 Network driver using the MDIO layer of the Linux kernel
GRPCI or GRPCI2 PCI Host support
GRUSBHC USB 1.1/2.0 Host controller
GRUSBDC USB 1.1/2.0 Device controller
GRVGA Graphical Frame Buffer
GRPS2 mouse/keyboard PS/2 controller
GRCAN and OCCAN implements the Linux socket CAN 2.0b interface
GRGPIO supports the generic General Purpose I/O model of Linux
SPICTRL supports SPI master interface through the spi-fsl driver
I2CMST support I2C master interface through the i2c-ocores driver

## Slide 9: Buildroot distribution
LEON Buildroot 2022.02-1.x
LEON specific documentation about Buildroot is found in the LEON Buildroot User's Manual
RAM images with MKLINUXIMG
Create bootable ROM images from the RAM images with MKPROM
GNU GCC toolchain

## Slide 10: Hardware Requirements
LEON3, LEON4 or LEON5
SPARC V8 mul/div
MMU
GPTIMER for system clock
IRQMP or IRQ(A)MP for interrupt support
D-Cache snooping
FPU
32 MiB RAM